## Slide 1
RQ2
Same-City Latency:
DOMESTIC CONTENT
The gap is small. In Karachi, ISPs A, G, and F reach Pakistani-hosted sites at a median 18.4, 20.3, and 41.3 ms, a 2.2x spread. In Lahore, ISPs I, D, H, and C run a median 17.5 to 23.7 ms, a 1.4x spread.
2.2x / 1.4x
Karachi / Lahore spread, domestic sites
CDN CONTENT
In Karachi, ISP A reaches CDN content at a median 4.4 ms with 61.5% served locally, ISP G at 78.0 ms with 41.0% local, and ISP F at 129.8 ms with none local, a 29.8x spread. In Lahore, ISP C reaches a median 2.8 ms with 84.6% local, while ISPs D, H, and I cluster at 91 to 95 ms with zero local hits, a 34x spread.
29.8x / 34x
Karachi / Lahore spread, CDN sites
Every ISP in a city sits at roughly the same physical distance from where a cache would be, so a gap this large can't be a distance problem, it's a peering choice. Cross-checked against Cloudflare's own edge for ISP C: 31 of 33 sites answered from a Pakistani point of presence, with 0 to 3 ms handshakes, physically impossible from outside the country. The same two sites answered from Singapore for every other network.