## Slide 1
RQ4
A Local Path Exists:
Three sites account for 86% of all tromboned traces. ISP A reaches every one of them without leaving the country on every single round, while six of the nine operators trombone to them on essentially every round. This is a measurement, not a blind spot: ISP A's probe resolves as many mid-path hops as the probes that do register tromboning.
One financial-services site makes the mechanism concrete: ISP A reaches it in 5.4 ms over a domestic connection. Six of the nine operators reach the same server only by routing abroad first, through Oman for ISP F and through Singapore for ISP D and ISP I, arriving 15 to 33 times slower. Every path that leaves the country still enters through the same ISP A edge, so the domestic path already carries real traffic, it isn't just possible in principle.
415 / 16 / 13
of 444 probe-site pairs: never / always / sometimes tromboned
8 / 37
sites ever confirmed tromboned from any vantage; none exceeds 90% of rounds