## Slide 1
National Block-Routing Census
Does traffic sent to a Pakistani small ISP actually stay in Pakistan?
• Standalone exploratory run
• 48 small ISPs · 747 announced blocks · 7 vantage points
• Rayan Atif · September 2026
1 / 18

## Slide 2
THE QUESTION
What we mean by a detour
[ diagram — see slides.html ] A real case from the June run. Both ends are in Lahore. Seven of the eight probed addresses stay inside Pakistan; the eighth leaves the country and comes back.
That excursion is the thing we are counting — across every block of every small ISP, from several different starting points.
2 / 18

## Slide 3
READ THIS FIRST
Probes are vantage points, not targets
Destinations — what we census Vantage points — where we measure FROM
Who · 48 small/local ISPs (PTA FLL licensees) · 7 Atlas probes, mostly at large ISPs
Role · The thing being measured · The place the traceroute starts
Chosen for · Completeness — every block · Transit diversity — one per upstream
PTCL, Nayatel, Cybernet, Nova and Z-Com are vantage points. They are never destinations. The targets are always the 747 blocks of the 48 small ISPs.
Why several vantage points? Because a detour depends on the sender's transit — the same block can be local from one network and foreign from another.
3 / 18

## Slide 4
SELECTION &MIDDOT; 1 OF 2
How we get to 747 blocks
[ diagram — see slides.html ] Every number is derived from a file in the repo, not estimated.
• Roster from <span class='mono'>pk_isp_fll_list.csv; prefixes from RIPEstat; blocks written to <span class='mono'>blocks_all.csv
• The 18 that announce nothing are excluded from probing — and kept as a finding
• Top 5 ISPs hold 432 of 747 blocks (58%), so per-ISP rates lead, not block averages
4 / 18

## Slide 5
SELECTION &MIDDOT; 2 OF 2
How we get to 7 vantage points
Stage Count How that number was obtained
PK probes known to the project · 16 · Exp 4.1 roster + Exp 07 panel map
connected · 12 · Atlas probe API status, checked 2026-09-01
path-visible under TCP/80 · 10 · drops 7764, 62224 — recorded ICMP-filtered
deduplicated by transit · 7 · one probe per distinct upstream AS
• Selection rule: one vantage per distinct transit
• Plus two deliberate duplicates — a second Transworld and a second Cybernet — to test that behaviour clusters by transit rather than assume it
• Since June: two probes died, one came back. The roster needed re-checking
5 / 18

## Slide 6
METHOD
The sampling rule
• The unit is the BGP prefix, not the address. Every address in an announced block shares one route — so the block is what we census
• Every block is kept. None ranked, pruned or sampled away — a census claim needs completeness. Reduction happens inside blocks, never across them
• We probe K addresses inside each block — the next three slides are what K is
• Density comes free — how many of the K replied, from the same pass
Prefix-as-unit and density come from TASS (Klick et al., IMC 2016). We invert their rule: TASS drops low-density prefixes; a census must keep every one.
6 / 18

## Slide 7
K &MIDDOT; 1 OF 3
K is how many addresses we probe per block
[ diagram — see slides.html ] A /24 holds 256 addresses. Probing all of them, for 747 blocks from 7 vantage points, would be 1.3 million traceroutes.
So we probe K evenly spaced addresses instead and let the BGP route do the generalising: every address in the block shares one route, so a handful should tell us how the whole block is reached.
“Should” is the word doing the work. The next slide tests it.
7 / 18

## Slide 8
K &MIDDOT; 2 OF 3
Two real blocks, same eight positions
[ diagram — see slides.html ] Left-to-right, each dot is one probed address. Red left the country; green stayed.
• Top: the assumption holds. All 8 agree, so any 2 of them would have given the same answer — K could safely be small
• Bottom: the assumption breaks. One address in the block routes abroad while its neighbours do not. Pick the wrong 2 and you record this block as clean
8 / 18

## Slide 9
K &MIDDOT; 3 OF 3
How often does the assumption break?
Measured on the June run — 1,758 block-and-vantage pairs that got the full K=8:
Outcome Share Meaning
All probed addresses agree · 79.4% · the block has one route — small K is safe
Addresses disagree · 20.0% · the block is genuinely split
No usable answer · 0.6% · all eight silent or inconclusive
• One block in five is split. “The route to a block” is not always a well-defined thing — which is itself a finding, and one nobody has published
• On the blocks that are unambiguous, a random K=2 reproduces the K=8 verdict 98.6% of the time
• So K=2 gets the verdict right and the picture wrong. It cannot see that a block is split, because with two samples there is nothing to compare
• Decision: keep K=8. A 20% split rate is too high to sample away. Reduce vantages or rounds if the run needs shrinking — never K
9 / 18

## Slide 10
CLASSIFICATION &MIDDOT; 1 OF 2
What counts as a detour
What we call tromboning is what the measurement literature calls a routing detour — a path between two endpoints in one country that leaves and returns.
• Edmundson et al., 2016 — Characterizing and Avoiding Routing Detours Through Surveillance States. Establishes the detour as a systematic property of interdomain routing, and how to identify it from traceroute paths
• Gupta et al., PAM 2014 — Peering at the Internet's Frontier: ISP Interconnectivity in Africa. The direct regional antecedent: African traffic detouring via Europe because local interconnection was missing
• This census asks that same question of Pakistan
10 / 18

## Slide 11
CLASSIFICATION &MIDDOT; 2 OF 2
How we decide it left the country
Geolocation is used — but never on its own. Every foreign-hop claim is gated by RTT.
Rule Value Why
Foreign hop must also be slow · ≥ 40 ms · Router geolocation databases disagree (Gharaibeh, IMC 2017), so a country code alone is not evidence. RTT bounds how far a hop can be (Gueye et al., 2006)
Inter-hop jump · ≥ 60 ms · PK→Singapore measures ~60–90 ms — no domestic leg does that
Any hop RTT · ≥ 70 ms · Clear of the domestic ceiling; PK→Europe is ~100–130 ms
Stays local · < 45 ms · Domestic ceiling plus queueing headroom
Known artifact · AS6327 · Shaw CPE hop on the Nova probe — physically in PK at ~1.5 ms
• Thresholds are ours, calibrated to observed Pakistani RTTs. The principles are from the literature above
• The RTT backstop matters: 1,191 of the June run's 2,002 detours were caught this way, where the foreign hop never replied at all
11 / 18

## Slide 12
BASELINE
What the first run found
Exp 4.1 ran a full pass on 2026-06-27 — 18,260 probes, 7 vantage points, 696 of 747 blocks. Every figure below is a value count over that file.
Verdict Count Share
Local · 15,451 · 84.6%
Detour — caught by RTT backstop · 1,191 · 6.5%
Detour — foreign hop seen · 811 · 4.4%
Inconclusive · 807 · 4.4%
Detours, combined · 2,002 · 11.0%
Only 2,007 of 18,260 targets answered — 11%. Small-ISP blocks are mostly empty, exactly as the method assumes.
12 / 18

## Slide 13
BASELINE
The spread is the interesting part
By destination ISP By vantage point
Bliss Communication · 64.5% · Cybernet Haripur · 46.3%
Pace Telecom · 27.4% · PTCL Karachi · 38.4%
Brain Telecom · 21.1% · Cybernet Karachi · 10.5%
Trans World ES · 2.4% · Z-Com Lahore · 7.5%
LINKdotNET · 0.6% · Nayatel Islamabad · 4.0%
• Destinations range over two orders of magnitude — not a uniformly broken market, but a handful of badly-connected operators
• The vantage range is as wide as the destination range. Where you measure from matters as much as who you measure
13 / 18

## Slide 14
WHY AGAIN
The first run cannot be quoted
Coverage was badly unbalanced across vantage points — an 8× range in probe counts.
Vantage point Probes in the run
Z-Com Lahore · 4,609
Nova Lahore · 4,264
Nayatel Islamabad · 3,204
Cybernet Karachi · 2,084
Orbit Faisalabad · 2,012
PTCL Karachi · 1,525
Cybernet Haripur · 562
• Cybernet Haripur's 46.3% rests on 562 probes; Z-Com's on 4,609
• Each vantage saw a different, non-random subset — the rates are not comparable
• Only 594 of 696 blocks got the full K=8, so the split rate is measured on a subset
• Equal coverage per vantage is the point of re-running.
14 / 18

## Slide 15
SIZING
What the run comes to
Measured in traceroutes: 747 blocks × K addresses × S vantage points.
Stage Design Traceroutes
Pilot, once · K=8, 150 blocks, 6 vantages · 7,200
Census round × 3 · K=8, all 747 blocks, 6 vantages · 35,856 each
Total · 114,768
• Holding K at 8 is what the 20% split rate buys — and it is not negotiable without giving up split detection entirely
• If the run must shrink, drop a vantage or a round. Both lose something you can name; cutting K loses something you cannot see
• Paced under the 100-concurrent cap with randomised inter-launch delay — the same good-citizen discipline TASS argues for
15 / 18

## Slide 16
PLAN
Six phases
[ diagram — see slides.html ] Each phase has an exit criterion; nothing proceeds until the line beneath it is true.
Phase 2 re-measures the split rate on this exact population before the full census commits to it — the 20% figure comes from a subset of the June run, and deserves confirming on a clean, balanced sample.
16 / 18

## Slide 17
PAYOFF
What we might find
• A per-ISP detour rate and its real spread — quotable, because balanced
• Whether the vantage or the destination dominates. If it is the pair, the fix is bilateral peering; if the destination, that ISP's transit contract
• Who the detour transits through — PTCL or Transworld, per ISP
• Which foreign exchange it surfaces at — Equinix Singapore, DE-CIX, Omantel
• How often a single block splits across two routes — the June data says one in five, and nobody has published that for anywhere
• How sparse small-ISP address space really is
• Whether any trace touches PKIX or PIE — the panel found 0 of 222,944
• Announced-but-dark blocks, and the 18 licensed ISPs announcing nothing
17 / 18

## Slide 18
HONESTY
Limits we state up front
• Density is an active-address proxy, not traffic — Atlas cannot see bytes. Report “% of active address space”, never “% of traffic”
• A single round is a snapshot — rates are quoted as a range across rounds
• Geolocation is used, but never alone. The residual risk is a hop that is both mis-geolocated and genuinely slow
• Transit clustering is an assumption, only partly tested
• The FLL roster includes a few large and LDI members — flagged, not dropped
• Block sizes are not uniform — 22 of 747 are larger than /24, so the eight positions are computed per prefix length
• Every run ships a readable routes file next to the CSV. No verdict without the paths to check it against
18 / 18